## Slide 1: PCI TOI
    http://oliveryang.net
Compiled by Oliver Yang
Nov, 2017

## Slide 2: Agenda
PCI/PCIe Basic
PCIe errors handling
Case study - analysis PCIe errors
References

## Slide 3: Transition from PCI/PCI-X to PCIe

## Slide 4: PCI Throughput
Bandwidth(Gbps) = Frequency(Mhz) x bit(Bytes)
PCI / PCI-X | 32bit 33Mhz | 32bit 66Mhz | 64bit 66Mhz | 64bit 133Mhz
Bandwidth | 1.056 Gbps | 2.112 Gbps | 4.224 Gbps | 8.512 Gbps

## Slide 5: PCIe Throughput
GT/s vs. Gbps
  PCIe 1.x and 2.x use 8b/10b encoding
  PCIe 3.x uses 128/130 encoding.
Bandwidth(Gbps) = Per lane(Gbps) x Number of Lane
Real bandwidth is much slower because of overhead of PCIe itself
  One x8 PCIe 2.x slot only could hold dual ports 10G NIC
  One x8 PCIe 3.x slot only could hold four ports 10G NIC
Link Bandwidth | Raw Bit Rate x1 | x1 | x8 | x32
PCIe 1.x | 2.5 GT/s | 2Gbps | 16Gps | 64Gps
PCIe 2.x | 5.0 GT/s | 4Gbps | 32Gps | 128Gps
PCIe 3.x | 8.0 GT/s | 8Gbps | 64Gps | 256Gps

## Slide 6: PCI Express Mechanicals

## Slide 7: PCI vs. PCIe
PCI uses a shared parallel bus
  Bandwidth shared between devices on the bus
  Only one device may own the bus at any time
  Large number of parallel signals
  Wait states may be added by Initiator or Target
PCI-Express uses a serial point to point interconnect
  Full bandwidth dedicated to that link
  No need for arbitration
  Low number of signals
  No wait states

## Slide 8: PCIe Link
Port
  A group of transmitters and receivers located on the same chip that define a link
Lane
  A set of differential signal pairs, one pair for transmission and one pair for reception
Link
  A dual-simplex communications path between two components
  A xN link is composed of N lanes

## Slide 9: PCIe – Packet Based Protocol

## Slide 10: Transaction Layer
Responsible for
  Post and Non-Posted transactions
    Memory read/write, IO read/write, Configuration read/write etc.
  Managing link flow control
  Enforcing ordering and Quality of Service(QoS)
  Power management control/status
Header Information may include
  Address/Routing
  Data transfer Length
  Transaction descriptor
End to End CRC checking provides additional security(optional)

## Slide 11: Physical Link and Data Link Layers
Packets are transmitted serially
Credit based Flow Control
  Each device transmits periodic flow control packets to inform transmitter of buffer space
  Ensures that receiving device has buffer space for the packet
ACK/NAK ensure correct delivery of data
Different link status for power management
Can re-train the link in the event of catastrophic failure
  Only one or some of the lanes may be corrupted
  Retraining may allow fall back to lower bandwidth system.

## Slide 12: PCIe Fabric

## Slide 13: PCIe Terminologies
RC (Root Complex)
  A defined PCIe System Element that includes
    A Host Bridge
    Zero or more Root Complex Integrated Endpoints
    Zero or more Root Complex Event Collectors (Support RC EPs)
    One or more Root Ports.
Root Port
  A PCI Express Port on a Root Complex that maps a portion of the Hierarchy through an associated virtual PCI-PCI Bridge.
Switch
  A defined System Element that connects two or more Ports to allow Packets to be routed from one Port to another.
  To configuration software, a Switch appears as a collection of virtual PCI-to-PCI Bridges.
EP (Endpoint)
  A Function that has a Type 00h Configuration Space header.

## Slide 14: Domain:Bus:Device.Function
Domain
  Address range[0-65535]
  Each Domain have its separate bus range [0-255]
  x86 only have one PCI Domain: 0
Bus
  Address range [0-255]
  Devices from RC is attached to bus 0
  x86 could have multiple RCs, but all of RCs shared [0-255] bus range.
Device
  Address range [0-31]
Function
  Address range [0-7]

## Slide 15: PCI Address spaces
Address spaces
  Configuration Space (Accessed by Bus/Device/Function)
    Configuration Access Mechanism#1
      - Legacy in/out to IO ports 0xCF8 and 0xCFC.
    MMIO (memory mapped IO)
      - ACPI MCFG table provide the base address.
  Memory Space (Accessed mov instructions)
    Pointed by 32bit or 64bit BARs which are initialized by BIOS or OS
  IO Space (Accessed by in/out instructions)
    Pointed by IO BARs which are initialized by BIOS or OS
    Legacy space with size limitations.
Usages
  Config Space is standard for OS device enumeration and management.
  Memory and IO Spaces are device private

## Slide 16: 4K PCIe Config Space Layout

## Slide 17: PCI Config Space [0 - 63]
Two header types
  Type 0 - for regular EPs
  Type 1 - for switches and bridges
Device Identification
  VendorID: PCI-SIG assigned
  DeviceID: Vendor self-assigned
  Subsystem VendorID: PCI-SIG
  Subsystem DeviceID: Vendor
Address Decode controls
  Software reads/writes BARs to determine required size and maps appropriately
  Memory, I/O, and bus-master enables

## Slide 18: PCI Config Space [63 - 255]
Linked list
  Follow the list! Cannot assume fixed location of any given feature in any given device
  First entry in list is stored at offset of 0x34h in PCI config space.
  Features defined in their related specs:
    PCI-X
    PCIe
    PCI Power Management
    Etc…

## Slide 19: PCI Config Space [256 - 4095]
PCI Express only
Linked list
  Follow the list! Cannot assume fixed location of any given feature in any given device
  First entry in list is *always* at 100h
  Features defined in PCI Express specification

## Slide 20: PCI Hole and DRAM Remap

## Slide 21: PCIe INTx/MSI/MSI-X Differences
INTx
  PCIe defined the INTx messages to emulate INTx (INTA/B/C/D pins) assertions
  On x86, INTx messages will target to IOAPIC in PCH/South Bridge
  On x86 IOAPIC sends a Intel defined interrupt message to North Bridge
  LAPIC within the CPU die will receive INTx eventually
MSI
  Each PCIe functions config space has a PCIe MSI capability structure which allow up to 32 MSI vectors. All of 32 vectors share a same MSI address and MSI data pair, which means all 32 vectors target a same CPU core.
  MSI address and MSI data are initialized by OS interrupt vector allocation code
  PCIe device write the MSI data to MSI address by using a PCIe DMA write
  On x86, MSI address is the LAPIC address
  On x86, MSI data a Intel defined format, which defined interrupt delivery mode.
MSI-X
  Similar with MSI, but MSI-X capability structure allows up to 2048 vectors, and each MSI-X vectors defines the separate MSI address and data pairs, which could target to different CPU cores.

## Slide 22: Legacy PCI Interrupt on x86

## Slide 23: Message Based PCIe Interrupts

## Slide 24: MSI Address and Data on x86

## Slide 25: x86 DMA Transactions in PCIe
There are 4 possible DMA transactions
  Device memory to host memory
    PCIe DMA write transaction, memory write TLP
  Host memory to device memory
    PCIe DMA read transaction, memory read TLP
  Device memory to device memory
    PCIe peer to peer
  Host memory to host memory
    Not PCIe related.
    Supported by Intel CPU uncore DMA engine since Nehalem
PCIe DMA
  PCIe devices are bus master devices who can start a DMA transaction
  Each PCIe devices might have multiple built-in DMA engines
  On x86, without IOMMU support, DMA address is equal to MMU physical memory address
  If IOMMU enabled, a DMA address is an IO address. IOMMU translate an IO address to a MMU physical address

## Slide 26: PCI Bus Transactions

## Slide 27: Sandy Bridge Board

## Slide 28: Agenda
PCI/PCIe Basic
PCIe errors handling
Case study - analysis PCIe errors
References

## Slide 29: PCIe Errors Classification
PCIe Errors
Correctable Errors
Uncorrectable Errors
Fatal Errors
Non-Fatal Errors

## Slide 30: PCIe Errors Registers in Config Space
PCI Config Space
Legacy PCI
PCIe AER
CE Status
UE Status
Device Specific
Device Status
Secondary Status(Bridge only)

## Slide 31: PCI Device Status Register

## Slide 32: PCIe AER(Advance Error Reporting) Registers

## Slide 33: AER CE Status and Mask Registers

## Slide 34: AER UE Status and Mask Registers

## Slide 35: AER UE Severity Registers
Red color indicates the Fatal UEs

## Slide 36: PCIe Error Signaling
PCIe error signaling
  Completion Status other than success: UR, CA, CRS
  Error Messages: ERR_COR, ERR_NONFATAL, ERR_FATAL
  Error Forwarding, aka Data Poisoning
Error Interrupts
  System interrupts
    SMI - Handled by BIOS SMI interrupt handler
    NMI – Handled by OS NMI interrupt handler
      x86 standard NMI
      Vendor customized NMI
  Root Port device interrupts
    MSI or INTx handled by OS PCIe AER bus driver

## Slide 37: PCIe error signaling control
PCIe errors signaling could be controlled at different levels
  EP, Switch, Root Port
    AER CE/UE mask registers
    #SERR enable in PCI command register
    Device control registers in PCIe capability
  Root Port only
    Root Error Command register
    Root Control register

## Slide 38: PCIe Error Handling on Linux
PCIe AER bus driver handles all of PCIe CEs and UEs
  Negotiate with BIOS by ACPI _OSC method and get error handling control
  Disable SMI and register per Root Port MSI or INTx interrupts handlers.
  Handled errors interrupts with below strategies
    CE - Error logging and clear the registers
    Non-fatal UE
      - Disable all drivers associated within the device hierarchy
      - Error logging and registers dump
      - Call driver callbacks to reset the PCIe devices
      - Enable all affected drivers again if recover success
    Fatal UE
      - Disable all drivers within the device hierarchy
      - Error logging and registers dump
      - Call driver callbacks to log errors, and reset PCIe links, devices
      - Enable all affected drivers again if recover success

## Slide 39: Agenda
PCI/PCIe Basic
PCIe error handling
Case study - analysis PCIe errors
References

## Slide 40: Kernel panic for PCIe UEs – part I
On a x86 box, below command could trigger a kernel panic
  # dd if=/dev/mem of=/dev/null
The panic just means the system is panicked by HW errors, which could be either a HW fault or a software(driver) bug.
Look at the SEL logs to understand what HW errors are detected
  It was the completion abort PCIe UEs reported by device 84:0.0
    # grep HL bios.txt
    ELOG(109) -N- Completer Abort Status Bus:84H Dev:00H Fn:00H SID:FFFFFFFFH FEP:0FH HL:D0CF1D27CE200000800808FF00000002H
  The HL field in SEL log is PCIe TLP header log dump, which is actually from the TLP packet that caused the error.
  Now decode the header log: D0CF1D27CE200000800808FF00000002
    00000002 is the first 4(0-3) bytes of TLP header which tells us this TLP is a Memory Read Request TLP, and packet header has 3DW length(12bytes). So the D0CF1D27 is useless.
    800808FF tells us the PCIe TLP Requester(device) ID is 80:1.0 which is the PCIe Root Port.
    CE200000 is 32bit memory address according to Memory Read Request TLP packet format.
    Run lspci, we found that CE200000 is the start address in PLX switch memory(BAR0).
      # lspci -s 84:0.0 -vvv | grep -i reg
      Region 0: Memory at ce200000 (32-bit, non-prefetchable) [size=128K]
    Then we know PLX switch(84:0:0) send PCIe Root Port(80:1.0) a completion abort TLP, indicate the its device register read failure happened at memory address CE200000
  This HW failure should be HW/FW problems, as PLX bar0 is not owned by Linux OS.

## Slide 41: Kernel panic for PCIe UEs – part II

## Slide 42: Agenda
PCI/PCIe Basic
PCIe error handling
Case study - analysis PCIe errors
References

## Slide 43: References for this TOI material
PCI Express System Architecture (Book)
PCI Express Base Specification Revision 3.0
PCI Local Bus Specification Revision 3.0
The PCI Express Advanced Error Reporting Driver Guide HOWTO

## Slide 44: Q&A