## Slide 1: Linux NUMA Optimization TOI
    http://oliveryang.net
Oliver Yang
Feb, 2016

## Slide 2: Agenda
Overview
Kernel Facilities
Known Gaps
Opportunities

## Slide 3: Nodes, Sockets, Cores, Threads

## Slide 4: 2/4/8 Sockets Servers

## Slide 5: CPU NUMA Affinity
x86 changes since Nehalem
  Memory controller is integrated in die
  Has local and remote memory access
Worst case NUMA-node relative latency
  Intel 4 socket / 4 node: 1.5x
  AMD 4 socket / 8 node: 2.7x
  8 socket / 8 node: 2.8x
  32 node blade system: 5.5x

## Slide 6: Device NUMA Affinity
Changes after the Sandy Bridge
  No I/O hubs
  PCIe Root-Complex is in the die
  Devices connected to CPU directly
NUMA Node

## Slide 7: Why NUMA Affinities?
1. DMA
2.Interrupt
3. Mem Read
4. Mem Write

## Slide 8: Agenda
Overview
Kernel Facilities
Known Gaps
Opportunities

## Slide 9: Key Requirements
Device affinity
  DMA Memory locality
    Are DMA buffers close to the devices?
  Interrupt locality
    Are interrupts close to DMA buffers?
CPU affinity
  Host Memory locality
    Are memory buffers close to the running threads on the processors?
  Scheduling locality
    Are processes/threads close to its memory buffers?
  Protocols stacks (Network/IO etc..) locality
    Are data locality could be kept in the same NUMA nodes in the stack?

## Slide 10: DMA Memory Locality
Kernel buffer allocation
  dev_to_node VS. numa_node_id
    dev_to_node: get device numa node from device tree
    numa_node_id: get memory numa node per current CPU id
  Use dma_alloc_coherent directly
  Specify device numa node id in kernel APIs
    Use__netdev_alloc_skb instead of alloc_skb (not work for 3.2)
    int node = dev->dev.parent ? dev_to_node(dev->dev.parent) : -1;
    skb = __alloc_skb(length + NET_SKB_PAD, gfp_mask, 0, node);
    Use kmalloc_node instead of kmalloc
    int node = dev->dev.parent ? dev_to_node(dev->dev.parent) : -1;
    data = kmalloc_node(rx_buf_sz, GFP_KERNEL, node);
    Use alloc_pages_node instead of alloc_pages
User space buffer allocation
  No standard way, but could be done with kernel customizations.

## Slide 11: Interrupt Locality
Hardware IRQ
  Capabilities of different type of interrupts
  Local APIC interrupt delivery mode in Linux kernel
    Logical mode when CPU <= 8
      Local APIC chipset will do irq balance among 8 CPUs
      No NUMA affinity issues under this mode on latest x86 platform
    Physical flat mode when CPU > 8
      One interrupt vectors just can be bound to one CPU at a time.
      IRQ balance can break NUMA affinity
Soft IRQ
  After kernel code triggers it, a soft IRQ will be fired on the same core
    IRQ balance could impact the affinity of soft IRQ as well
Type | Max Vectors | Bound to multi-CPUs | Shared
INTx | 1 | No | Yes
MSI | 32 | No | No
MSI-X | 2048 | Yes | NO

## Slide 12: Host Memory Locality
Kernel memory allocation
  Slab allocator always returns memory from local NUMA node
    kmalloc and kmem_cache_alloc are NUMA aware
    kmalloc VS. kmalloc_node
      kmalloc allocates memory from local NUMA node per caller’s CPU.
      kmalloc_node allocates memory per node arguments, which could be any of NUMA nodes.
  Page allocator
    alloc_pages returns page from local NUMA node by default
    alloc_pages VS. alloc_pages_node
User space memory allocation
  Application hugetlb pages
    OS kernel can do NUMA aware hugetlb reservation
  Standard malloc in glibc also considers NUMA affinity
    Kernel page fault will try to return the page from local NUMA node first
      Local fault - memory on same node as CPU
      Remote fault - memory on different node than CPU

## Slide 13: NUMA Aware Kernel Memory Allocator
CPU
Cache
Layer
Slab
Layer
Page
Allocator
Numa node 0
Zone
Zone
Zone
Numa node 1
Zone
Zone
Zone
kmem_cache0
  Socket 0
CPU 0
CPU 1
Numa node 0
kmem_cache1
Socket 0
CPU 0
CPU 1
Numa node 0
kmem_cache0
Socket 1
CPU 2
CPU 3
Numa node 1
kmem_cache1
Socket 1
CPU 2
CPU 3
Numa node 1

## Slide 14: Scheduling Locality
Scheduler is NUMA aware
  Trade-off between affinity/locality and CPU availabilities.
    Scheduling domain are based on ACPI table
      Support SMT->SMP->NUMA topology and hierarchy
    Threads migration policy reflects to different scheduling domain
      Hyper thread CPUs level: No NUMA affinity issues
      Physical CPUs level: lose cache locality but has the NUMA affinity
      NUMA node level: Lose both cache locality and NUMA affinity
  Short running tasks could have better localities
  Threads migration might break the affinities for long running processes
    Threads wakeup could trigger threads migration (Major reasons in Linux OS)
    Runq load balance could be driven periodically by kernel.
Avoid tasks migration to get better localities
  Bind kernel thread to a specific CPU
    Use kthread_create_cpu instead of kthread_create
  Bind user processes to a specific CPU
    Use mbind() and set_mempolicy() system call

## Slide 15: Summary
Major NUMA features are available
  Kernel APIs are NUMA aware
  Core kernel services are NUMA aware
There are some gaps…
  Performance profiling tools
  Micro-benchmarks
    Throughput VS. Latency
  Had a NUMA mechanism in kernel, but lack of end-to-end affinity from kernel to user space
    DMA buffer affinity
    Interrupt affinity
    Kernel threads affinity (CPU/Cache/Memory)
    Application threads affinity (CPU/Cache/Memory)

## Slide 16: Agenda
Overview
Kernel Facilities
Known Gaps
Opportunities

## Slide 17: How To Identify Gaps
Full stack efforts, need check OS whole data path
  Hardware
    SLIC placements vs. QPI/PCIe bandwidth
  Firmware
    Key ACPI tables
      ACPI SRAT for CPU affinity information
      ACPI SLIT for NUMA domain information
      ACPI DSDT table for device affinity information
  Kernel & Drivers
    DMA affinity
    Interrupt affinity
    Kernel threads affinity
      Thread modeling
      Threads migrations
    Memory allocation
  Application
    User process affinity
      Thread modeling
      Threads migrations
    Memory allocation

## Slide 18: Full Stack View
Network
NIC Drivers
IO
Multipath
SAS driver
TCP/IP
Socket APP
SCSI mid layer
RAID Driver
Block
Kernel
Scheduler
Memory management
Device management

## Slide 19: Kernel
Device affinity
  Interrupt affinity
    Current irqbalance are not good enough.
      How can it work with TCP flow and GUTs
  DMA affinity
    Had the bug in DMA buffer affinity code path.
    Need evaluate DMA buffer affinity perf differences on Apollo
    DMA affinity can be determined by user space
CPU affinity
  Kernel memory management
    Need investigate recent NUMA scheduling features in mainline
  Scheduling
    Need investigate thread migration features in mainline
Profiling tools
  Need port some tools: NUMAtop/Some perf event features/IRQstat etc.
  Need investigate how to leverage tracepoints

## Slide 20: Network
Device affinity
  There is a trade-off between CPU availabilities and DMA buffer affinity
    Not all device drivers are optimized for DMA buffer affinity.
      For example, ixgbe doesn’t support, but bnx2x support
    How to set interrupts affinity when enable multiple device queues
      Stop using old irqbalance.
CPU affinity
  Very big gap for data copy between kernel and user space
    Kernel buffer and user buffer might be on different NUMA nodes
    Following kernel features need to be investigated,
      Flow Steering support
        RFS: Receive Flow Steering
        Flow director support in NICs (with multiple queues/interrupts)
    Scheduler tuning might be required.

## Slide 21: Idea Of Receive Flow Steering
CPU on which transmits for a flow occur is “remembered”
On receive for that flow, remembered cpu is looked up and packet steered to that CPU

## Slide 22: Network – Flow Director On Intel NIC

## Slide 23: Agenda
Overview
Kernel Facilities
Known Gaps
Opportunities

## Slide 24: Kernel Investigations – NUMA tools
NUMA profiling tools
  numactl
  numastat
  numad
  Sysfs
  Lstopo
  NUMAtop: https://01.org/numatop
  Top(NUMA version): https://gitorious.org/procps/procps
  Irqstat: https://github.com/lanceshelton/irqstat
  perf mem-loads event – available in 3.10 kernel
  c2c data-sharing tool(c2c == “cache to cache”)

## Slide 25: NUMA Top