## Slide 1: Kernel Memory Corruption Debug Based On SLAB Implementation
Oliver Yang
Jan 15, 2014
http://oliveryang.net

## Slide 2: Agenda
Basic concepts
Debugging methods
Case study
Potential improvements

## Slide 3: Agenda
Basic concepts
Debugging methods
Case study
Potential improvements

## Slide 4: Memory corruption causes
Hardware bugs
  X86 Machine Check errors
    CPU
    DIMM
    QPI
  PCIe errors
Some legacy or low end x86 box’s RAS protection had the big gaps
  Lots of CFDs caused by DIMM UEs and CPU errors
  Platform SEL logs might not have debug information

## Slide 5: Memory corruption causes
Software bugs
  Use before initilaization
  Use after free on heap, stack, global
    Reference invalid memory
    Double free
  Out of bound memory access
    Heap overflow
    Stack overflow
    Global overflow
  Data race
    Race conditions on memory modifications

## Slide 6: Challenges
Memory corruption: one of most intractable issues
  Hard to get root causes by a core dump file
    The source of the memory corruption and its manifestation may be far apart, making it hard to correlate the cause and the effect.
  Difficult to reproduce
    Symptoms appear under unusual conditions, making it hard to consistently reproduce the error
Kernel memory debugging is more difficulty
  Difficult to triage due to cross component boundary
  Lack of debugging facilities and tools

## Slide 7: Kernel memory APIs
Buddy System (pages)
get_user_pages
SLAB allocator
alloc_pages __get_free_pages
kmalloc
kmem_cache_alloc
vmalloc
io_remap

## Slide 8: SLAB Intro

## Slide 9: Slab Structure
kmem_cache
array_cache[N_CPUS]
kmem_list3[N_NODES]
slabs_full
slabs_partial
slabs_free
array_cache *shared
array_cache *alien
Per-CPU local cache
Global Slab Layer
Page allocator

## Slide 10: Slab - Layered Design
CPU
Cache
Layer
Slab
Layer
Page
Allocator
Numa node 0
Zone
Zone
Zone
Numa node 1
Zone
Zone
Zone
kmem_cache0
  Socket 0
CPU 0
CPU 1
Numa node 0
kmem_cache1
Socket 0
CPU 0
CPU 1
Numa node 0
kmem_cache0
Socket 1
CPU 2
CPU 3
Numa node 1
kmem_cache1
Socket 1
CPU 2
CPU 3
Numa node 1

## Slide 11: Slab memory layout

## Slide 12: SLAB debugging use cases
Use-after-free
  Poison, check at next alloc
  If off_slab and nPAGEs, record the call stack of last free, then unmap the slab page
Use-before-initialization
  Poison, check at debugging time
Double free, check the memory outside of object
  Redzone, mark INACTIVE at free time
  Bufctl, mark FREE at free time
Buffer overflow
  Redzone, check redzone at free
Memory Leak
  Traverse all the slab, and aggregate the callers (STORE_USER)

## Slide 13: Object layout for debugging
Object
redzone1
8 bytes
caller IP
8 bytes
redzone2
8 bytes

## Slide 14: Redzone
#define RED_INACTIVE 0x09F911029D74E35BULL /* when obj is inactive */
#define RED_ACTIVE 0xD84156C5635688C0ULL /* when obj is active */
Initialization
set redzone INACTIVE
ctor()
! INACTIVE. (X)
Allocation
! INACTIVE. (X)
set redzone ACTIVE
Deallocation
check redzone
  ACTIVE. Y
  INACTIVE (double free)
  else, overwritten
set redzone INACTIVE
Destroy
! INACTIVE. (X)

## Slide 15: Poison
#define POISON_INUSE 0x5a /* for use-uninitialised poisoning */
#define POISON_FREE 0x6b /* for use-after-free poisoning */
#define POISON_END 0xa5 /* end-byte of poisoning */
Initialization
6b 6b … 6b a5
Allocation
! (6b 6b … 6b 5a) (X)
ctor()
5a 5a … 5a a5
Deallocation
6b 6b … 6b a5
Destroy
! (6b 6b … 6b a5) (X)
Panic
NN 5a … NN a5

## Slide 16: Other Debug Features
Save caller IP
State for management array tacking
  BUFCTL_END
  BUFCTL_FREE
  BUFCTL_ACTIVE
  SLAB_LIMIT

## Slide 17: Agenda
Basic concepts
Debugging methods
Case study
Potential improvements

## Slide 18: Kernel Core Analysis
Identify corruption location
Confirm corruption pattern
Search potential culprit
Nail down issue by code

## Slide 19: Identify corruption location
Understand the scenario
Study the source code
Verified the scenario in kernel core files

## Slide 20: Confirm Corruption Pattern
Get to familiar with the corrupted data structure
  Learn related data structure and source code
Jump out the box - dump the raw memory pages
  Basic knowledge of kernel memory allocators
    Slab/Slub/vmalloc/ioremap/page allocators
Are they similar with any known corruption patterns?
  Is it a possible corruption pattern caused by HW error?
    If yes, confirm from BIOS SEL logs
  For patterns caused by SW bugs, please refer to page 5.

## Slide 21: Search potential culprit
Search the pointer if culprit owns the pointer
  Per corruption pattern, determine possible pointer address
  Run search -k <pointer address> to get all references
  Using kmem and rd to determine the references owners
Search the corruption data if culprit owns that pattern
  Per corruption pattern, determine the basic corrupted data
  Run search -k <data pattern> to get all references
  Using kmem and rd to confirm the references owners

## Slide 22: Nail down issue by code
Narrow down the source code in possible culprit
  Per corruption pattern, determine data structure
  Per corruption pattern, determine the related memory API
  Find the memory signature if possible
Any debug code could be enabled for catching bugs?
  Run the testing with debug code enabled

## Slide 23: Agenda
Basic concepts
Debugging methods
Case study
Potential improvements

## Slide 24: A Slab corruption bug - 1
Identify the corruption location
  Get the back trace, and find the panic location
    cache_alloc_refill+0x17b
  Dump the corrupted memory
    crash> slab ffff810262bf5040
    struct slab {
    list = {
    next = 0x20a00150463, <====== bad pointer
    prev = 0xffff810c0ec002c0
    },
    ……………………………..
  Understand why the corruption cause the panic
    Unable to handle kernel paging request at 0000020a0015046b

## Slide 25: A Slab corruption bug - 2
Confirm the corruption pattern
  Get to familiar with the corrupted data structure
    Slab struct is at or close to the page boundary
  Jump out the box - dump the raw memory pages
    Not only check the slab, but also dump the adjacent pages
  Are they similar with any known corruption patterns?
    Shouldn’t be HW bug, as the corruption pattern had the significant pattern
    It looked like the buffer overflow bug.

## Slide 26: A Slab corruption bug - 3
Correlate corruption with potential culprit
  Search the pointer if culprit owns the pointer
    The pointer address might be ffff810262bf4000 because,
      the corruption pattern seemed to start here.
      the kmem ffff810262bf4000 indicated it is not allocated by slab
      Search who reference the pointer?
        crash> search -k ffff810262bf4000
        ffff810262f03928: ffff810262bf4000
    Who is the owner of ffff810262f03928?
      crash> rd ffff810262f03920 -64 128
      Found the signature: qla2xxx_ts_11 and QLE2562

## Slide 27: Agenda
Basic concepts
Debugging methods
Case study
Potential improvements

## Slide 28: Improvements for memory corruption debug
Using debug kernel in…
  Kernel/Driver unit testing
  Release testing
Increase the debugability for kernel/driver
  Avoid to use the page allocator if SLUB/SLAB allocation is possible
  Consider to implement some debug features
    Create module/driver unique memory signature
    Introduce the redzone and posion code in module/driver
Use kernel debug features
  Replace Slab with Slub which enables SLUG_DEBUG
  Debug page alloc
  Kmemcheck
  KASAN

## Slide 29: Q&A
Thank you!